BR.W514 Series

Pilot operated self operated pressure control valve

INSTRUCTION

MANUAL

ZHEJIANG LASEN INTELLIGENT EQUIPMENT CO.,LTD

CATALOG

1. Product Overview and Features	2

2. Structure and Principle	2

2.1 Structure	2

2.2. Operation principle	3

2.3. Actuator Part	3

3. Installation and Maintenance	4

3.1. Installation	4

3.2 Use	4

3.3 Maintenance	4

4. Instructions for ordering	5

5. Appendix	6

Appendix I: Main technical parameters	6

Appendix II: Material of main parts	7

Appendix III. Size and weight of pilot operated self operated control valve	7

# Product Overview and Features

The pilot operated self operated pressure regulating valve (hereinafter referred to as pressure regulating valve) is a kind of self operated pressure regulating valve without external energy. It uses the energy of the controlled medium as the power source and introduces the detection actuator of the command to control the plug position of the pressure regulating valve, change the medium flow through the valve, and keep the pressure behind the valve at a constant value.

Features: The pressure setting value can be realized on the commander and can be adjusted at will during operation, so it is convenient, fast and labor-saving; the control precision is about twice as high as that of the general pressure regulating valve; the pressure reduction ratio is large; and the set pressure is low.

# Structure and Principle

## 2.1 Structure

The pilot operated self operated pressure regulating valve is composed of actuator, pilot valve, regulating valve, pressure pipe, etc., as shown in Figure 1.

1.Body  2. Seat  3. Plug 4. Stem 5. Seal sleeve 6. Gland 7. Bearing rod 8. Actuator 9. Spring 10. Pilot valve 11. Filter regulator 12. Pressure tap 13. Globe valve 14. Pressure tap

Fig  BR.W514 Series pilot operated self operated control valve’s internal structure

## 2.2. Operation principle

The pressure regulating valve is composed of director, main valve, throttle valve and filter regulator (see Fig. 1). The medium enters the valve body in the direction of arrow, and outputs after throttling by plug and seat. At the same time, the inlet medium enters into the valve body of the command device after being filtered and depressurized by the filter regulator, and then enters the upper and lower membrane chambers of the main valve actuator after being regulated by the commander. When the output pressure increases, the main valve is closed by the action of the director and throttle valve until the pressure behind the valve is reduced to the set value. Similarly, when the output pressure decreases, the main valve is opened by the action of the director and throttle valve until the pressure behind the valve rises to the set value.

## 2.3. Actuator Part

Sheet1  Main technical parameters of actuator

| Spec Mode | Diaphragm |
| --- | --- |
| Purpose | Regulation |
| Diaphragm Material | NBR, fluororubber, oil resistant rubber |
| Connection | M16×1.5 |
| Action Mode | The pressure rise valve opens , the pressure rise valve closes |
| Medium Temperature | -20～+120℃ |
| Standard valve accessories | Pressure pipe (including pressure tapping joint) |
| Optional valve accessories | Pressure tapping pipe, stop valve, pressure gauge, flange, gasket and fastener |

# Installation and Maintenance

## 3.1. Installation

- Before installation, check whether the product model and specification meet the requirements. The pipeline shall be cleaned to remove welding slag and sundries. The valve shall be installed vertically and vertically on the pipeline, and the medium flow direction shall be consistent with the arrow of valve body. If possible, bypass valves should be provided.

- In order to ensure the normal operation of the pressure regulating valve, a filter, pressure gauge and manual valve shall be set in front of the valve. The installation drawing is shown in Fig.2.

Fig2  Installation drawing of pressure regulating valve

## 3.2 Use

- Slowly open the inlet and outlet stop valves of the control valve to the maximum. At this time, due to the introduction of medium into the control valve, the pressure indication value can be observed.

- Gradually close the bypass valve, open the shell cover, and adjust the spring preload until the pressure indication value meets the process requirements.

- Lock the nut and cover the housing.

## 3.3 Maintenance

After the device is put into normal operation, there is no need for special maintenance, but the commander, throttle valve and filter pressure reducer should be cleaned regularly. If there is any fault, it should be treated according to sheet 2.

Sheet 2 common faults and troubleshooting

| Fault | Cause | troubleshooting |
| --- | --- | --- |
| The pressure cannot be controlled automatically | Control line blocked | Cleaning control pipeline |
|  | Throttle valve blocked | Dredge throttle valve |
|  | Rupture of diaphragm | Replace the diaphragm |
|  | The spring is broken | Replace the spring |
|  | The valve diameter is too small | Replace the valve |
| Pressure instability | The valve diameter is too large | Replace the valve |
|  | The valve diameter is too large or small | Replace the spring |

# Instructions for ordering

- Product model and name

- Nominal pressure

- Nominal diameter

- Pressure before and after the valve

- Mediumn, density and temperature

- Medium’s maximum, normal and minimum flow

- Inherent flow characteristics of valve

- Overall action mode, gas source pressure, signal range

- Valve body and trim material

- Explosion proof requirements

Accessories and other special requirement

# Appendix

## Appendix I: Main technical parameters

Sheet 3-1  BR.W514 series standard type

| Nominal diameter | 20 | 25 | 32 | 40 | 50 | 65 | 80 | 100 | 125 | 150 | 200 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Rated Kv | 7 | 11 | 20 | 30 | 48 | 75 | 120 | 190 | 300 | 480 | 760 |
| Rated stroke L(mm) | 8 | 10 | 12 | 20 | 22 | 25 | 25 |
| Inherent flow characteristics | Quick open |
| Differential pressure of valve during normal operation | ≥0.2MPa |
| Applicable media | Non corrosive gas(-20～120℃) |
| Pressure regulation range (KPa) | 0.14-2.0 1-6 5-10 9-15 12-19 18-25 22-30 28-35 32-40 38-50 48-60 58-72 70-100 |
| Adjustment accuracy | ±5% |
| Allowable leakage | Metal seal: Ⅳ(×Kv);Soft seal:Ⅵ(ACC GB/T4213-2008) |

Note: pressure regulation range can be customized according to customer requirements.

Sheet 3-2  BR.W514Series low flow type

| Nominal diameter | 20、25 |
| --- | --- |
|  | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 12 | 15 |
| Rated Kv | 0.02 | 0.08 | 0.12 | 0.20 | 0.32 | 0.5 | 0.8 | 1.2 | 1.8 | 2.5 | 4 |
| Rated stroke L(mm) | 5 |
| Inherent flow characteristics | Linear, Fixed linear | Quick open |
| Differential pressure of valve during normal operation | ≥0.2MPa |
| Adjustment accuracy | ±5% |
| Allowable leakage | Metal seal: Ⅳ(×Kv);Soft seal:Ⅵ(ACC GB/T4213-2008) |

Note: pressure regulation range can be customized according to customer requirements.

## Appendix II: Material of main parts

Sheet 4

| Part name | Material |
| --- | --- |
| Body, bonnet | WCB CF8 CF8M CF3 CF3M |
| Trim | 0Cr18Ni9(304);0Cr17Ni12Mo2(316) 00Cr17Ni14Mo2(316L) Above+R.TFE(Modified PTFE) Above+Stellite(Hardfacing stellite alloy) |
| Packing | O-ring (Material: NBR, fluororubber, oil resistant rubber) |
| Spring | 60Si2Mn |
| Diaphragm cap | Q235, SS |

## Appendix III. Size and weight of pilot operated self operated control valve

BR.W514 control valve  (Diaphragm actuator)

Sheet 5-1 Size of control valve Unit:mm

| DN | L | H | H1 | A |
| --- | --- | --- | --- | --- |
| DN | IN | PN16 ANSI150lb |  |  |  |
| 15 | 1/2″ | 184 | 709 | 70 | ¢308 ¢394 ¢498 |
| 20 | 3/4″ | 184 | 709 | 70 |  |
| 25 | 1″ | 184 | 709 | 60 |  |
| 32 | 1-1/4″ | 200 | 730 | 80 |  |
| 40 | 1-1/2″ | 222 | 740 | 85 |  |
| 50 | 2″ | 254 | 750 | 95 |  |
| 65 | 2-1/4″ | 276 | 777 | 110 |  |
| 80 | 3″ | 298 | 777 | 125 |  |
| 100 | 4″ | 352 | 820 | 133 |  |
| 125 | 5″ | 403 | 1000 | 163 |  |
| 150 | 6″ | 451 | 1120 | 188 |  |
| 200 | 8″ | 543 | 1155 | 200 |  |

Note：1. The size in the table is PN16 standard configuration data, if you need different pressure level parameters, please contact our company.

- Our company can customize and produce valve products under various harsh working conditions according to customers' requirements. If customers have no special requirements, we will supply according to standard configuration.

- Stop valve and pressure connection pipe are non-standard valve accessories, which can be selected according to customer requirements.

L1 and P in the sheet are the standard configuration of our company. Generally, P ≥ 6 × DN can also be configured according to customer requirements.

ZHEJIANG LASEN INTELLIGENT EQUIPMENT CO.,LTD ADD:No. 15 Mashan Road, Changkou Industrial Zone, Fuyang District, Hangzhou, Zhejiang Province TEL:0571-23252111/23291601 FAX:0571-23291602 WEB:www.lasen.com.cn POST CODE:311401